UDPtoDMX Protocol:

The commands have to be sent by UDP to Port 7000.
Easy way to send and receive UDP Packets for testing is https://packetsender.com/.

General Format:

header	typ	#	channel	#	value	#	speed_S	#	curve	#	speed_F

DMX	P	#	1	#	100	#	7	#	3	#	1

Orange is Optional

Examples:

DMXC2#129
DMXP3#55#1
DMXP3#56#2#2
DMXR1#3066012#1#1
DMXR1#3066012

Header:
always DMX

Typ:
P: percent (0-100)
C: direct (0-255)
R: RGB (loxone format: R + G * 1000 + B * 1000000)
V: tunable white (0-100): channel: WW, channel+1: CW
W: tunable white (0-100): channel: CW, channel+1: WW

Value:
Integer Value

speed_S:
Integer Value (0-255)

255: set Value immediately (no Fading)
1: Fast
99: Slow

+100: 4-times faster
+200: 8-times faster

see Time-Table

curve: (dimming curve)
Integer Value (0-3)
0: linear (0%=0, 50%=128, 100%=255)
1-3: “logarithmic” curve

see dimming curve graph

speed_F:
like speed_S, but it is used when dim-step is more than 10%
will be set so speed_S if the value is missing
this is for fast dimming (e.g. from 0% to 100%)

Time-Table:
(from 0% to 100% or 100% to 0%)
Speed	ms
1	591
2	1176
3	1749
4	2350
5	2890
6	3495
7	4061
…
98	57262

101	147
102	293
103	434
104	583
…

201	72
202	145
…
254	3691
255	0

Dimming curve:

Tunable white mode: